## Slide 1: Lens and propagation of uncertainty

## Slide 2: Prelab on uncertainty
So, how do we determine dA?

## Slide 3: Prelab on uncertainty
First go at it: A ± dA = (L ± dL) ∙ (W ± dW)
Just as likely to cancel as to add!
This feels uncomfortable
dL*dW | First Guess
4 | 84
16 | 176
12 | 172
16 | 216
A ± dA = LW ± LdW ± WdL + dLdW

## Slide 4: Prelab on uncertainty
Second go at it: A = L ∙ W ; dA is half the range between (L-dL) ∙ (W-dW) and (L+dL) ∙ (W+dW)
dL*dW | First Guess | Second Guess
4 | 84 | 80
16 | 176 | 160
12 | 172 | 160
16 | 216 | 200

## Slide 5: Prelab on uncertainty
Third go at it: A = L ∙ W ; dA is sum of percent uncertain for each term
dL*dW | First Guess | Second Guess | Third Guess
4 | 84 | 80 | 80
16 | 176 | 160 | 160
12 | 172 | 160 | 160
16 | 216 | 200 | 200

## Slide 6: Multivariable Uncertainty Propagation
This formula always works!
In general, this is a faultless formula.
Uncertainty propagation gets more complex as more variables depend on each other.
For example, for A that is a function of two variables L and W, then…

## Slide 7: Quick Derivative Review
signifies the partial derivative
Partial derivates work in mostly the same way that normal derivatives work, except that they involve functions of more than one variable.
The denominator shows the variable of interest. All other variables in the equation are treated as constants during partial derivation.
A trick to make this easier sometimes is to replace all other variables with specific numbers, like π, A, or 100, so long as you keep track of that.

## Slide 8: Prelab on uncertainty
Final answer:
dL*dW | First Guess | Second Guess | Third Guess | Final Guess
4 | 84 | 80 | 80 | 57
16 | 176 | 160 | 160 | 113
12 | 172 | 160 | 160 | 126
16 | 216 | 200 | 200 | 165
*Remember to follow proper conventions with rounding/sig figs when reporting uncertainty.

## Slide 9: [Lab 3] Propagation of Uncertainty

## Slide 10: [Lab 3] Propagation of Uncertainty

## Slide 11: Questions?

## Slide 12: Thin Lenses

## Slide 13: Helpful equations
Optical Power :
Optical Equation :
Optical equation goes by many names: lensmaker’s formula, thin lens equation, etc. and can use different variable symbols (p, s, o,)
P =

## Slide 14
Part 1:
  Test for one lens and the crystal ball
    Plan on testing multiple dos and dis
  Propagation of uncertainty
  Write summary δP/P for each lens on the board (smallest correct value will get bonus point)
Part 2:
  How lenses add () in the eye model

## Slide 15: Part 2:To find
Pasco Light source
do = object distance
di = image distance
+62mm

## Slide 16: Add a corrective lens
Pasco Light source
do = object distance
di = image distance
+62mm

## Slide 17: Take measurement again with corrective lens
Pasco Light source
+62mm
Corrective lens

## Slide 18: Extra Slides

## Slide 19: [Lab 3] Propagation of Uncertainty
Plot | L | dL | W | dW | A
A | 20 | 2 | 20 | 2 | 400
B | 20 | 4 | 20 | 4 | 400
C | 20 | 6 | 20 | 2 | 400
D | 40 | 4 | 10 | 4 | 400
So, how do we determine dA?

## Slide 20: [Lab 3] Propagation of Uncertainty
Plot | L | dL | W | dW | A
A | 20 | 2 | 20 | 2 | 400
B | 20 | 4 | 20 | 4 | 400
C | 20 | 6 | 20 | 2 | 400
D | 40 | 4 | 10 | 4 | 400
dL*dW | First Guess | 
4 |  | 
16 |  | 
12 |  | 
16 |  | 
First Guess:

## Slide 21: [Lab 3] Propagation of Uncertainty
Plot | L | dL | W | dW | A
A | 20 | 2 | 20 | 2 | 400
B | 20 | 4 | 20 | 4 | 400
C | 20 | 6 | 20 | 2 | 400
D | 40 | 4 | 10 | 4 | 400
dL*dW | First Guess | 
4 | dA = 84 | 
16 | dA = 176 | 
12 | dA = 172 | 
16 | dA = 216 | 
First Guess:
Just as likely to cancel as to add!

## Slide 22: [Lab 3] Propagation of Uncertainty
Each uncertainty contributes to the total uncertainty proportional to the partial derivative (slope of f with respect to that variable)
Multiple sources don’t simply add but add “in quadrature”, since they are as likely to cancel as add
We will always give you the needed derivatives
For example, if f is a function of two variables, then…

## Slide 23: [Lab 3] Propagation of Uncertainty
Plot | L | dL | W | dW | A
A | 20 | 2 | 20 | 2 | 400
B | 20 | 4 | 20 | 4 | 400
C | 20 | 6 | 20 | 2 | 400
D | 40 | 4 | 10 | 4 | 400
dL*dW | First Guess | Final Answer
4 | dA = 84 | ≈57
16 | dA = 176 | ≈113
12 | dA = 172 | ≈126
16 | dA = 216 | ≈165
First Guess:
Final Answer:
*Remember to follow proper conventions with rounding/sig figs when reporting uncertainty.

## Slide 24: [Lab 3] Propagation of Uncertainty

## Slide 25: [Lab 3] Propagation of Uncertainty

## Slide 26: [Lab 3] Propagation of Uncertainty

## Slide 27: [Lab 3] Propagation of Uncertainty